## Slide 1: Herzlich Willkommen
International Energy Engineering | Solar Energy | Prof. Sirag Kartun
Group 1 :- 1. Ashish Manoj Mistari
2. Lakshmikantha Malode Ranganatharao
© 2024 OTH Amberg-Weiden

## Slide 2: Agenda
01
02
03
Geogrphical Location
Building Specification
Project Plan
06
07
08
Design of Layout
Comparison between
PV modules
Parameter Specefication
04
Load Assessment
09
Polysun Result
05
Introduction
10
Feasibility Study

## Slide 3
1. Introduction
1
Aim: “To design a cost-effective, efficient solar energy system”.
Objective :
Analysis of the site
Collection and Analysis of data
Forecasting and designing of the solar system
Economic calculations
Selection of the solar system

## Slide 4
2. Geographical Location
Country :- India
City :- Pune, Maharashtra.
Location Coordinates:- 21°20'01.1"N 74°33'22.1"E
Building type :- 2 Floor Apartment
Type of Building :- Residential
Area :- 1200
Usable Area :- 900
Orientation of Building :- South-West Facing
3. Building Specification
2
Source :- https://maps.app.goo.gl/uNLqEW6Sm1UzJp6r9?g_st=aw

## Slide 5
4. Project Plan
3
Task | Start Date | End Date | Duration Days | Progress
Study & Planning | 24-Mar | 31-Mar | 7 | Done
Project Initiation | 01-Apr | 08-Apr | 7 | Done
Location Selection | 09-Apr | 23-Apr | 14 | Done
Data Collection | 24-Apr | 08-May | 14 | Done
Feasibility Study | 09-May | 16-May | 7 | Done
Layout Design | 17-May | 31-May | 14 | Done
System Design | 01-Jun | 08-Jun | 14 | Done
Final Design | 09-Jun | 16-Jun | 7 | Done
Presentation Report | 17-Jun | 24-Jun | 7 | Done
Chart: Timeline
| Study & Planning | Project Initiation | Location Selection | Data Collection | Feasibility Study | Layout Design | System Design | Final Design | Presentation Report
Start Date | 45740 | 45748 | 45756 | 45771 | 45786 | 45794 | 45809 | 45817 | 45825
Duration Days | 7 | 7 | 14 | 14 | 7 | 14 | 14 | 7 | 7

## Slide 6
5. Load Assessment
Electricity Consumption data 2024
Month | Electricity Consumed (kWh)
January | 78
February | 83
March | 107
April | 130
May | 123
June | 140
July | 122
August | 148
September | 100
October | 126
November | 94
December | 86
Total | 1337
Chart: 
| January | February | March | April | May | June | July | August | September | October | November | December
Electricity Consumed (kWh) | 78 | 83 | 107 | 130 | 123 | 140 | 122 | 148 | 100 | 126 | 94 | 86
4
Source:- Maharashtra State Electricity Distribution Company Limited Light Bills

## Slide 7
Sun Path Diagram
5
Source :- https://maps.app.goo.gl/uNLqEW6Sm1UzJp6r9?g_st=aw
6. Design of Layout

## Slide 8
6. Design of Layout (continued)
6
Software :- Polysun
Source :- Polysun Software

## Slide 9
7. Comparison
7
Feature | Polycrystaline | Monocrystaline
Solar Panel Efficiency | Low Efficiency Rate 13% to 16% | High Efficiency Rate 16% to 23%
Appearance | Blue | Black
Cost | Less Expensive | More Expensive
Life Span | 25-35 years | 25-35 years
Temperature Coefficient | Low Temperature Coefficient | High Temperature Coefficient
Durability | Less Durable | Highly Durable
Roof Space | Requires more roof space | Works on Roofs with limited space
Source:- FreyrEnergy_Access Time & Date_17.15_19062025

## Slide 10
8. Parameter Specification
8
2. PV Module
1. Local Electricity Grid
Electricity Grid :- Three Phase (127V/220V, 50Hz,WYE)
Grid Configuration :- Three Phase star (WYE)
Nominal Voltage :- 220V
Nominal Frequency :- 50Hz
Source :- Polysun Software

## Slide 11
Tata Power Solar TP300
Electrical Parameters at Standard Test Conditions (STC)
Power Output Pmax (W) | 216.0
Voltage at PMAX VMPP (V) | 32.2
Current at PMAX IMPP (A) | 6.71
Open-circuit voltage Voc (V) | 39.4
Short-circuit current Isc (A) | 7.24
Electrical Parameters at NOCT
Source:- FreyrEnergy_Access Time & Date_17.15_19062025
8. Parameter Specification (continued)
9

## Slide 12
Temperature coefficient characteristics
Operating conditions
NOCT (ºC) | 47 ± 2
Module efficiency (%/ºC) | -0.06 ± 0.01
Temperature coefficient of PMAX (%/ºC) | -0.41
Temperature coefficient of VOC (%/ºC) | -0.32
Temperature coefficient of ISC (%/ºC) | 0.058
Maximum system voltage (UL & IEC) (V) | 1000 & 1000
Maximum series fuse rating (A) | 20
Limiting reverse current (A) | 20
Operating temperature range (ºC) | –40 and +85
Maximum static load (snow or wind) | 113 psf (5400 Pa)
Source:- FreyrEnergy_Access Time & Date_17.15_19062025
Tata Power Solar TP300
8. Parameter Specification (continued)
10

## Slide 13
8. Parameter Specification (continued)
11
3. Inverter
Max. recommended PV power (for module STC) | 4290W
Max. DC voltage | 550V
Start voltage | 80V
MPP voltage range | 65V-550V
Nominal voltage | 360V
No. of PV strings per MPP tracker | 1
Source :- Inverter_Growatt-MIC3300TL-X2_Access Time & Date_2040_24062025 , Polysun Software
Input Data :-

## Slide 14
AC nominal power | 3300W
Max. AC apparent power | 3300VA
Nominal AC voltage(range*) | 230V (180-280V)
AC grid frequency(range*) | 50/60 Hz (45-55Hz/55-65 Hz)
Max. output current | 14.3A
Adjustable power facto | 0.8leading…0.8lagging
THDi | <3%
AC grid connection type | Single phase
Output data (AC)
Max. efficiency | 97.6%
European efficiency | 97.1%
MPPT efficiency | 99.9%
Efficiency
8. Parameter Specification (continued)
Growatt MIC 3300TL-X2
Source :- Inverter_Growatt-MIC3300TL-X2_Access Time & Date_2040_24062025 , Polysun Software
12

## Slide 15
8. Parameter Specification (continued)
13
4. Battery
Source :- Polysun Software

## Slide 16
9. Result
Electricity Produced by PV Modules
Electricity Consumption
14
Source :- Polysun Software

## Slide 17
Electricity supplied to the Grid
Electricity from the Grid
15
9. Result (continued)
Source :- Polysun Software

## Slide 18
10. Feasibility Study
16
Source :- Contral Government Incentives_Access Time & Date_18.45_24062025 ,
Funding Schemes under Government of India
Pradhan Mantri Surya Ghar Yojana (PMSG)
  Support benefits 30000 ₹ per kilowatt upto 2 kW power system.
  Additional support 18000 ₹, if system power goes above 3 kW.
  Maximum 78000 ₹ will be supported from Government of India.
  Low interest loan financing from the Bank at 7 % interest rate under 3 kW power PV system.
  These incentive schemes are only for residential households.

## Slide 19
10. Feasibility Study (continued)
Investment Parameters
PV Module cost | 8700.00 | ₹/Module
Number of Module | 10.00 | Module
Total PV Module cost | 87000.00 | ₹
Inverter Cost | 19500.00 | ₹
Battery Cost | 252000.00 | ₹
Installation Cost | 30.00 | ₹ / W
Total installation Cost | 90000.00 | ₹
Total Lifespan | 27.00 | years
Polysun Data_with battery |  | 
Yield Photovoltics | 4245.00 | kWh
Electricity Demand | 1337.00 | kWh
Polysun Data_without battery |  | 
Yield Photovoltics | 4469.00 | kWh
Self Consumption | 693.00 | kWh
Energy cost |  | 
From grid | 10.00 | ₹
To grid | 3.00 | ₹
Source :- PV module Cost Access Time & Date 11.30_19062025 , Growatt_MIC3300TL-X_Access Time & Date_ 11.45_19062025
17

## Slide 20
CAPEX Calculation with Battery |  |  | 
Appliances | No. of Units required | Per unit cost (₹) | Total Cost (₹)
PV Modules | 10.00 | 8700.00 | 87000.00
Battery | 1.00 | 252000.00 | 252000.00
Inverter | 1.00 | 19500.00 | 19500.00
Installation per W |  | 9000.00 | 90000.00
Total CAPEX |  |  | 448500.00
CAPEX Calculation without Battery |  |  | 
Appliances | No. of Units required | Per unit cost (₹) | Total Cost (₹)
PV Modules | 10.00 | 8700.00 | 87000.00
Inverter | 1.00 | 19500.00 | 19500.00
Installation |  | 9000.00 | 90000.00
Total CAPEX |  |  | 196500.00
1. CAPEX (without incentive)
18
Source:- PV module Cost Access Time & Date 11.30_19062025 , Growatt_MIC3300TL-X_Access Time & Date_ 11.45_19062025
2. CAPEX (with incentive)
CAPEX Calculation_with_battery | 370500.00 | ₹
CAPEX Calculation_without_battery | 118500.00 | ₹
10. Feasibility Study (continued)

## Slide 21
3. OPEX
OPEX Calculation with Battery |  | 
Maintenance Cost | 13455.00 | ₹ / a
OPEX Calculation without Battery |  | 
Maintenance Cost | 5895.00 | ₹ / a
4. LCOE
LCOE_with_Battery | 6.40 | ₹ / kWh
LCOE_without_Battery | 2.30 | ₹ / kWh
19
10. Feasibility Study (continued)

## Slide 22
Condition :- 1 (with Battery 100% Feed In) |  |  | 
Parameter | kWh | ₹ / a | € / a
Self Consumption | - | - | -
Elec. From External Grid | 1337.00 | 13370.00 | 134.82
Feed-in tariff | 4245.00 | 12735.00 | 128.42
Savings | - | -635.00 | -6.40
Condition :- 2 (With Battery 33% consumption based on demand) |  |  | 
Parameter | kWh | ₹ / a | € / a
Self Consumption | 441.21 | 4412.10 | 44.49
Elec. From External Grid | 895.79 | 8957.90 | 90.33
Feed-in tariff | 3803.79 | 11411.37 | 115.07
Savings |  | 6865.57 | 68.65
10. Feasibility Study (continued)
20
Payback Period | 53 years

## Slide 23
Condition :- 3 (With Battery 66% consumption based on demand) |  |  | 
Parameter | kWh | ₹ / a | € / a
Self Consumption | 882.42 | 8824.20 | 88.98
Elec. From External Grid | 454.58 | 4545.80 | 45.84
Feed-in tariff | 3362.58 | 10087.74 | 101.72
Savings |  | 14366.14 | 143.66
Condition :- 4 (Without Battery) |  |  | 
Parameter | kWh | ₹ / a | € / a
Self Consumption | 693.00 | 6930.00 | 69.88
Elec. From External Grid | 644.00 | 6440.00 | 64.94
Feed-in tariff | 3776.00 | 11328.00 | 114.23
Savings |  | 11818.00 | 118.18
10. Feasibility Study (continued)
21
Payback Period | 25.7 years
Payback Period | 10 years

## Slide 24
Thank You

## Slide 25: Professional Report Without Battery
Source :- Polysun Software

## Slide 26: Professional Report With Battery
Source :- Polysun Software